## Slide 1
Three parallel branches
LAB 1 STEP 1 OF 5 SCHEMATIC FIRST
1 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 1 of 27
Schematic first. Try the connections before opening the next breadboard view.
YOUR STATION
3 V (2×AAA) pack, three 220 Ω resistors, board, meter, jumpers and paper.
UNPOWERED CHECK
Check board continuity and each isolated resistor in Ω. Record R1–R3.
SCHEMATIC BUILD
Connect each resistor between the same positive and negative source nodes.
CHECK
Build with the pack disconnected. Try the schematic before viewing the next slide.
+
−
B1
3 V
2×AAA
R1
220 Ω
R2
220 Ω
R3
220 Ω
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–115. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-build.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 2
Three parallel branches
LAB 1 STEP 2 OF 5 BREADBOARD CHECK
2 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 2 of 27
R1 left, R2 middle, R3 right. Green, blue and orange feeds share the + rail.
YOUR STATION
3 V (2×AAA) pack, three 220 Ω resistors, board, meter, jumpers and paper.
UNPOWERED CHECK
Check hole groups, rail breaks and each isolated resistor in Ω. Record R1–R3.
BUILD
Place R1–R3 across the center gap at 8, 15 and 22. Feed each from + and return each to −.
CHECK
Record on paper. Check actual rail continuity and ask for a wiring check before powering.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–115. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-build.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 3
Voltage across each branch
LAB 1 STEP 3 OF 5 SCHEMATIC FIRST
3 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 3 of 27
Schematic first. Try the connections before opening the next breadboard view.
METER SETUP
Use V/Ω and COM. Select DC volts. Power the checked circuit.
SOURCE READING
Measure across the pack and record its actual voltage.
BRANCH READINGS
CHECK
Record source V, V1, V2 and V3. Keep probe tips from bridging adjacent strips.
+
−
B1
3 V
2×AAA
R1
220 Ω
R2
220 Ω
R3
220 Ω
V
+
COM
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–115. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-voltage.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 4
Voltage across each branch
LAB 1 STEP 4 OF 5 BREADBOARD CHECK
4 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 4 of 27
Probes span R2. Keep every branch connected during voltage measurements.
METER SETUP
Use V/Ω and COM. Select DC volts. Power the checked circuit.
SOURCE READING
Measure across the pack and record its actual voltage.
BRANCH READINGS
CHECK
Record source V, V1, V2 and V3. Keep probe tips from bridging adjacent strips.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–115. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-voltage.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 5
Branch voltage results
LAB 1 STEP 5 OF 5
5 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 5 of 27
Copy the table. Predict from your measured source voltage.
ACROSS | PREDICT (V) | MEASURE (V)
Source | Your source reading | Your reading
R1 | Your prediction | Your reading
R2 | Your prediction | Your reading
R3 | Your prediction | Your reading
CHECK
Why does each branch receive the full source voltage?
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–115. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 6
Total current measurement
LAB 2 STEP 1 OF 5 SCHEMATIC FIRST
6 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 6 of 27
Schematic first. Try the connections before opening the next breadboard view.
POWER OFF
METER IN THE GAP
Select suitable fused DC current input/range. Red to − rail, COM to pack negative.
CHECK AND MEASURE
Ask for a check. Power and record total mA. Disconnect before moving any leads.
CHECK
Never place a current meter across the pack. Follow your meter’s fused jack and range labels.
+
−
B1
3 V
2×AAA
A
+
COM
R1
220 Ω
R2
220 Ω
R3
220 Ω
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 115–117. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-total-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 7
Total current measurement
LAB 2 STEP 2 OF 5 BREADBOARD CHECK
7 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 7 of 27
The ammeter completes the pack return. It carries all three branch currents.
POWER OFF
METER IN THE GAP
Select suitable fused DC current input/range. Red to − rail, COM to pack negative.
CHECK AND MEASURE
Ask for a check. Power and record total mA. Disconnect before moving any leads.
CHECK
Never place a current meter across the pack. Follow your meter’s fused jack and range labels.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 115–117. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-total-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 8
Current through one branch
LAB 2 STEP 3 OF 5 SCHEMATIC FIRST
8 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 8 of 27
Schematic first. Try the connections before opening the next breadboard view.
POWER OFF AND RESTORE
METER IN THAT GAP
Put the fused current meter in that gap. Red toward +, COM toward R2. Check and measure.
REPEAT FOR R1 AND R3
CHECK
Finish with power off, all feeds restored and the red lead back in V/Ω.
+
−
B1
3 V
2×AAA
R1
220 Ω
A
+
COM
R2
220 Ω
R3
220 Ω
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 115–117. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-branch-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 9
Current through one branch
LAB 2 STEP 4 OF 5 BREADBOARD CHECK
9 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 9 of 27
R2 measurement shown. R1’s green and R3’s orange feeds remain connected.
POWER OFF AND RESTORE
METER IN THAT GAP
Red current lead to + rail. COM to R2’s upper strip. Power after a check.
REPEAT FOR R1 AND R3
CHECK
Finish with power off, all feeds restored and the red lead back in V/Ω.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 115–117. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-branch-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 10
Current results
LAB 2 STEP 5 OF 5
10 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 10 of 27
Use I(A) = source V ÷ branch Ω. Multiply by 1000 for mA.
CURRENT | PREDICT (mA) | MEASURE (mA)
R1 branch | Your calculation | Your reading
R2 branch | Your calculation | Your reading
R3 branch | Your calculation | Your reading
Source total | Add predictions | Your reading
CHECK
Add your measured branch currents. How close is the sum to your measured total?
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 115–117. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 11
Isolated parallel resistance
LAB 3 STEP 1 OF 4 SCHEMATIC FIRST
11 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 11 of 27
Schematic first. Try the connections before opening the next breadboard view.
SOURCE REMOVED
Disconnect both pack leads from the circuit. Keep all three parallel branches.
METER SETUP
Put red in V/Ω and black in COM. Select Ω.
MEASURE THE NETWORK
CHECK
Use Ω mode only on an unpowered circuit with the source disconnected.
PACK DISCONNECTED
Ω
V/Ω
COM
R1
220 Ω
R2
220 Ω
R3
220 Ω
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 118–122. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-ohms.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 12
Isolated parallel resistance
LAB 3 STEP 2 OF 4 BREADBOARD CHECK
12 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 12 of 27
The pack is completely isolated. The ohmmeter spans the parallel network.
SOURCE REMOVED
Disconnect both pack leads from the circuit. Keep all three parallel branches.
METER SETUP
Put red in V/Ω and black in COM. Select Ω.
MEASURE THE NETWORK
CHECK
Use Ω mode only on an unpowered circuit with the source disconnected.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 118–122. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/parallel-ohms.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 13
One, two and three branches
LAB 3 STEP 3 OF 4
13 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 13 of 27
ONE BRANCH
Keep the source disconnected. Remove the blue R2 and orange R3 positive feeds. Measure Ω.
TWO BRANCHES
Restore the blue R2 feed. Leave the orange R3 feed open. Measure Ω at the same two nodes.
THREE BRANCHES
Restore the orange R3 feed. Measure Ω again. Calculate predictions using your resistor readings.
CHECK
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 118–122. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 14
Parallel resistance results
LAB 3 STEP 4 OF 4
14 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 14 of 27
Copy the table. Use Rt = 1 ÷ (1/R1 + 1/R2 + …) for the connected branches.
CONNECTED | PREDICT (Ω) | MEASURE (Ω)
R1 only | Your R1 | Your reading
R1 and R2 | Your calculation | Your reading
R1, R2 and R3 | Your calculation | Your reading
CHECK
What happens to total resistance as you add a parallel path?
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 118–122. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 15
Two unequal branches
LAB 4 STEP 1 OF 5 SCHEMATIC FIRST
15 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 15 of 27
Schematic first. Try the connections before opening the next breadboard view.
POWER OFF
Branch A uses R1 alone. Branch B uses R2 and R3 in series.
TWO COMMON NODES
Connect the whole of each branch between source positive and negative.
PATH CHECK
Keep only two complete branches. Ask for a wiring check before power.
CHECK
+
−
B1
3 V
2×AAA
R1
220 Ω
R2
220 Ω
R3
220 Ω
BRANCH A
BRANCH B
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 116–117,120–123. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/unequal-build.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 16
Two unequal branches
LAB 4 STEP 2 OF 5 BREADBOARD CHECK
16 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 16 of 27
The orange link joins D15 to J22. A is about 220 Ω. B is about 440 Ω.
POWER OFF
Branch A uses R1 alone. Branch B uses R2 and R3 in series.
REWIRE BRANCH B
Remove R3’s orange + feed and R2’s black return. Link R2 lower to R3 upper.
TRACE THE PATHS
CHECK
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 116–117,120–123. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/unequal-build.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 17
Unequal branch measurements
LAB 4 STEP 3 OF 5 SCHEMATIC FIRST
17 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 17 of 27
Schematic first. Try the connections before opening the next breadboard view.
DC VOLTS FIRST
Measure across A and across all of B. Record both. Then disconnect the pack.
CURRENT IN BRANCH B
Insert the fused meter in B’s input. Red toward +, COM toward R2. Check and read mA.
CURRENT IN BRANCH A
Power off. Restore B’s input. Move the meter into A. Check, measure and restore with power off.
CHECK
Disconnect for every lead move. Use a suitable fused current range. Return red to V/Ω.
+
−
B1
3 V
2×AAA
R1
220 Ω
A
+
COM
R2
220 Ω
R3
220 Ω
BRANCH A
BRANCH B
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 116–117,120–123. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/unequal-branch-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 18
Unequal branch measurements
LAB 4 STEP 4 OF 5 BREADBOARD CHECK
18 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 18 of 27
Branch B current shown. Its two series resistors carry the same current.
DC VOLTS FIRST
Measure across A and across all of B. Record both. Then disconnect the pack.
CURRENT IN BRANCH B
CURRENT IN BRANCH A
CHECK
Disconnect for every lead move. Use a suitable fused current range. Return red to V/Ω.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 116–117,120–123. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/unequal-branch-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 19
Unequal branch results
LAB 4 STEP 5 OF 5
19 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 19 of 27
Use the voltage across the whole branch in I = V ÷ Rbranch.
CURRENT | PREDICT (mA) | RESULT (mA)
A: R1 | Your calculation | Your reading
B: R2 + R3 | Your calculation | Your reading
Total: A + B | Add predictions | Add readings
CHECK
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 116–117,120–123. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 20
An open parallel branch
LAB 5 STEP 1 OF 5 SCHEMATIC FIRST
20 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 20 of 27
Schematic first. Try the connections before opening the next breadboard view.
RESTORE FIRST
OPEN ONLY R2
DC VOLTAGE TEST
Power after a check. Record R1, R3, R2 and the voltage across the missing feed.
CHECK
The V meter spans the open feed. Keep the opening in place while taking its voltage.
+
−
B1
3 V
2×AAA
R1
220 Ω
OPEN
R2
220 Ω
R3
220 Ω
V
+
COM
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–118,127. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/open-branch-voltage.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 21
An open parallel branch
LAB 5 STEP 2 OF 5 BREADBOARD CHECK
21 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 21 of 27
The meter spans the open blue-feed gap. The two other branches still operate.
RESTORE FIRST
OPEN ONLY R2
DC VOLTAGE TEST
Power after a check. Record R1, R3, R2 and the voltage across the missing feed.
CHECK
Use V/Ω and COM. The gap test uses a voltmeter while the blue feed remains removed.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–118,127. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/open-branch-voltage.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 22
Total current with R2 open
LAB 5 STEP 3 OF 5 SCHEMATIC FIRST
22 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 22 of 27
Schematic first. Try the connections before opening the next breadboard view.
POWER OFF
Power off. Leave R2’s input open. Open the source negative return for the current meter.
TOTAL CURRENT TEST
Use the fused current setup from Lab 2. Red to − rail, COM to pack negative.
RECORD AND RESTORE
Record total mA. Power off, restore pack return and blue feed. Return red to V/Ω.
CHECK
Compare this total with Lab 2. Never bridge the + and − rails with the current meter.
+
−
B1
3 V
2×AAA
A
+
COM
R1
220 Ω
OPEN
R2
220 Ω
R3
220 Ω
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–118,127. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/open-total-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage. This editable wiring schematic precedes the matching physical breadboard view. Attempt the circuit with power off, then compare the next slide. A is a current meter in series, V is a voltmeter across two points, Ω is an unpowered resistance measurement. Symbols identify electrical connectivity, not physical terminal locations.

## Slide 23
Total current with R2 open
LAB 5 STEP 4 OF 5 BREADBOARD CHECK
23 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 23 of 27
The meter is in the source return. The missing blue feed still opens only R2.
POWER OFF
Leave R2’s blue feed removed. Open the pack’s negative return at the − rail.
TOTAL CURRENT TEST
Use the fused current setup from Lab 2. Red to − rail, COM to pack negative.
RECORD AND RESTORE
Record total mA. Power off, restore pack return and blue feed. Return red to V/Ω.
CHECK
Compare this total with Lab 2. Never bridge the + and − rails with the current meter.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–118,127. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop. Circuit: assets/open-total-current.fzz, native Fritzing 1.0.8 bundled parts, schematic connection model rather than a physical-build test. Holder artwork depicts one cell but the actual classroom source is one two-AAA pack, nominal 3 V.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 24
Open branch results
LAB 5 STEP 5 OF 5
24 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 24 of 27
Use Labs 1–2 for the normal circuit. Record the open-feed gap voltage separately.
QUANTITY | NORMAL | R2 OPEN
R1 voltage (V) | Lab 1 reading | Your reading
R3 voltage (V) | Lab 1 reading | Your reading
R2 voltage (V) | Lab 1 reading | Your reading
Total current (mA) | Lab 2 reading | Your reading
CHECK
Why do the other branches keep working? What if the common source return opened?
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 114–118,127. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 25
Power from recorded readings
LAB 6 STEP 1 OF 3
25 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 25 of 27
USE THE NORMAL CIRCUIT DATA
Use branch voltages from Lab 1 and branch/total currents from Lab 2. Keep the pack disconnected.
CONVERT AND CALCULATE
Divide mA by 1000 to get A. For each resistor, calculate P(W) = branch V × branch I(A).
SOURCE POWER
Calculate source V × total I(A). Compare it with P1 + P2 + P3.
CHECK
Use the three-parallel-branch readings. Keep unequal-branch and open-branch data separate.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 125–126. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 26
Power results
LAB 6 STEP 2 OF 3
26 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 26 of 27
Copy the table. Show current in amperes before calculating watts.
LOAD | VOLTS | AMPS | POWER (W)
R1 | Lab 1 | Lab 2 ÷ 1000 | Calculate
R2 | Lab 1 | Lab 2 ÷ 1000 | Calculate
R3 | Lab 1 | Lab 2 ÷ 1000 | Calculate
Source | Source reading | Total ÷ 1000 | Calculate
CHECK
Does the sum of branch watts match the source watts within measurement limits?
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 125–126. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.

## Slide 27
Ratings and station reset
LAB 6 STEP 3 OF 3
27 / 27
DC Theory Chapter 5 Student labs 3 V pack (2×AAA) Slide 27 of 27
Ask for the verified resistor power rating. Record each rating in watts.
RESISTOR | CALCULATED (W) | RATING (W) | BELOW RATING?
R1 | Your calculation | Verified value | Yes / No
R2 | Your calculation | Verified value | Yes / No
R3 | Your calculation | Verified value | Yes / No
CHECK
Finish with the pack disconnected, normal feeds restored and the red lead in V/Ω.
Notes: Record predictions, readings with units and explanations on paper. Follow your actual meter input and range labels. Disconnect before wire or lead changes.
Source: NJATC DC Theory, 3rd edition, ISBN 9781935941125, Chapter 5, printed pp. 125–126. Book figures cropped from supplied Ch05DCTheory photos. See assets/sources.json for exact source photo and crop.
Classroom source: ONE nominal 3 V battery pack containing TWO 1.5 V AAA cells in series. Use actual measured loaded voltage and component values for calculations. The one-cell breadboard artwork does not change the source voltage.